Demodulator

     The demodulator module takes the symbol lookup dictionary and an input symbol array (presumably corrupted by noise effects) and attempts to recover the binary string. The module uses a simple maximum likelihood algorithm. The incoming array is correlated with each item in the symbol dictionary. The binary string resulting in the highest correlation value is returned. In the case of 8-bit symbols this requires 256 multiplications and array summations. This results in a fairly high time cost. The module could be improved by doing a bit by bit estimation, but the cost would be that the MSK modulation would no longer perform as if though it is coherently detected. The MSK modulation generated by the symbol dictionary module has coherent phase between bits, but not between multiple symbols. Correlating the received signals with the original stored symbol maintains coherent phase.

Usage:

from demodulator import *
demodinstance = demodulator(symboldict)
outputstring = demodinstance.run(inputarray)

symboldict: The symbol dictionary used to store the symbol waveforms
inputarray: An input waveform