Real Time Audio Performance

     Processing arrays through the channel simulator requires (relatively) large amounts of time, especially if they are passed through the fading channel. The serial time processing budget for each sample, given an audio sampling rate of 11025 Hz, is only 90μs. AWGN processing, by itself with samples = 200, requires 153μs. The time budget analysis is shown below.

Audio Processing Time Budget
Time Between Samples	90μs
AWGN	(123μs)
Fading	(2876μs)
Modulation & Demodulation	(5831μs)
Net	(8770μs)

     Clearly, using this process for simulating the channel will not yield success. If the sample processing could be pipelined, so that processing for sample N+1 begins before processing for sample N starts, then it may be possible to have additional processing cause only a lag in the input to output audio duration. Multi-threading was attempted to solve the problem, but was unable to compensate for the large time requirements. Python's multi-threading module provides only minimal performance gains for this application. Real-time audio channel simulation may be realizable with a radically different Python architecture, such as the use of DSP type filter implementations and faster C-based data types (in contrast with the numpy arrays), or by implementing the entire program in C. This method, however, was not successful in meeting the originally desired outcome.